## Slide 1: Course content
Introduction
Regulatory texts governing occupational health and safety
Basic concepts
Occupational risk prevention approach
Occupational risk assessment approach
Single occupational risk assessment document: development, implementation and follow-up, critical analysis, re-evaluation
Promotion of workplace health
Consideration of high-risk workers, enhanced medical surveillance
Conclusion
5

## Slide 2: Context and issues – Statistics
Some figures on health and safety at work worldwide (Source: International Labour Organization)
Every 15 seconds, a worker dies from a work-related accident or disease.
Every 15 seconds, 153 workers are victims of a work-related accident.
Every day, 6,300 people die from a work accident or work-related illness — that’s more than 2.3 million deaths per year.
In the construction sector, at least 60,000 fatal accidents occur every year worldwide — that’s one death every 10 minutes.
321,000 people die each year from occupational accidents.
317 million non-fatal workplace accidents occur each year.
160 million non-fatal occupational diseases occur per year.
17

## Slide 3: Context and issues – Statistics
Some figures on occupational health and safety (Source: Ministry of Labour, Employment, and Social Security)
In 2013, Algeria recorded 619 work-related deaths, a decrease of 8% compared to the year 2012.
640 cases of occupational diseases were reported, 27% of which were caused by chemical risks.
The number of workplace accidents was around 50,000, representing less than 1% of the total number of workers.
The expenses of the National Social Insurance Fund for Salaried Workers (CNAS), related to work accidents and occupational diseases, exceeded 20 billion DZD each year.
So what is the solution to minimize the increase in these figures?

## Slide 4: Context and issues –Occupational Risk assessment is a necessity
hazardous sources
Harm to people
Damage to property
Damage to the environment
Finding
Major accidents
Workplace accidents
Occupational diseases
Environmental degradation
Issues
Economic: Direct costs (workplace accidents, occupational diseases) and indirect costs (lost time after an accident, reduced productivity).
Social and societal: Ethical concerns, employee demotivation (poor working conditions), damage to the company’s image (especially regarding environmental impact).
Legal: Liabilities, penalties.
Necessity
The assessment of occupational risks is an investment and an opportunity, not an expense.

## Slide 5: Context and issues – What does an occupational risk mean?
Occupational risks represent any risk originating from professional activity, that is, paid work, which is essential for living nowadays.
Any phenomenon or event that occurs in the workplace and presents a hazard to people is called an occupational risk.

## Slide 6: Basic concepts (1)
Health, Safety, Environment (HSE) is a field of technical expertise that monitors aspects related to occupational diseases and workplace accidents. An HSE manager is responsible for overseeing working conditions (environmental hygiene), preserving health by controlling physical factors (lighting, noise, dust, radiation, etc.), and ensuring that the work process does not create hazardous situations that could harm people or assets. They are also responsible for monitoring the strict application of standards related to health and safety.
Health: is defined in several references as the physical and mental well-being of workers. It concerns the prevention of occupational diseases.
Safety : A concept characterized by the absence of dangers capable of causing harm.
Note that this absence is not total, meaning that such dangers do exist, but in such a way that the resulting risks remain at an acceptable level. Here, we are talking about the prevention of workplace accidents.
Environment: It represents all the natural and cultural conditions in which living beings develop.
21

## Slide 7: Basic concepts (2)
Workplace accident: Whatever the cause, an accident that occurs as a result of or during the course of work, involving any person employed or working, in any capacity whatsoever, for one or more employers or business owners. Example: electric shock, fall, cut.
occupational disease is the result of short-term or long-term exposure to a risk associated with the normal performance of one’s job. Example: silicosis, musculoskeletal disorders.
Only the diseases listed in the tables annexed to the Decree of May 5, 1996, which establishes the list of diseases presumed to be of occupational origin, are officially recognized as occupational diseases.
Dangerous event: An event likely to cause harm or damage.
Harm (or Damage): Physical injury or impairment of health. This may result from a work accident or an occupational disease.
Exposure: A situation in which a person is subjected to one or more chemical or biological agents, or to physical phenomena such as noise or ionizing radiation, which may cause harm in the short or long term. Example: working in cold conditions.

## Slide 8: Basic concepts (3)
Dangerous situation: A situation in which a person is exposed to at least one hazardous event. This exposure may cause harm either immediately or over the long term.
Dangerous situation: Drilling while holding the workpiece by hand.
Use of a vise to prevent injury or damage.

## Slide 9: Exercise
Describe the dangerous situation given the following details:
Enclosed duct (protected against direct contact)
Good lighting
Acceptable noise level

## Slide 10: Basic concepts (4)

## Slide 11: Unsafe act and unsafe condition

## Slide 12: Near miss

## Slide 13: Basic concepts (5) – Example of severity
To assess the severity of a risk, there are four levels of severity:
Low: accident without work stoppage
Medium: accident with work stoppage
Serious: accident resulting in permanent disability
Very serious: death

## Slide 14: Basic concepts (5)- example of probability
To assess the likelihood of a risk, there are four levels of probability:

## Slide 15: Basic concepts (7)
Concept of Criticality / Criticality Grid: This concept is defined as the result of combining two dimensions — severity and probability of occurrence. It makes it possible to assess the magnitude of a risk. All risk levels are adjusted proportionally according to the importance of two dimensions — probability and severity — within a chart called the criticality grid. This grid serves as a kind of balance that allows us to weigh the risk and determine whether it is acceptable or unacceptable. Based on the results, a decision is made regarding the appropriate measures needed to control the risk.

## Slide 16: Exercise
Place a cross in the box corresponding to the correct answer:
 | Hazard | Risk | Occupational disease | Damage
Benzene |  |  |  | 
Dispersion of toxic substances |  |  |  | 
Burns |  |  |  | 
Tetanus |  |  |  | 
Corrosive substance |  |  |  | 
Fire |  |  |  | 
Skin irritation |  |  |  | 
Microorganism with infectious properties |  |  |  | 
Post-traumatic stress disorder (PTSD) |  |  |  | 29

## Slide 17: Solution
 | Hazard | Risk | Occupational disease | Damage
Benzene | + |  |  | 
Dispersion of toxic substances |  | + |  | 
Burns |  |  |  | +
Tetanus |  |  | + | 
Corrosive substance | + |  |  | 
Fire |  | + |  | 
Skin irritation |  |  |  | +
Microorganism with infectious properties | + |  |  | 
Post-traumatic stress disorder (PTSD) |  |  | + | 29

## Slide 18: Diagram of the process of harm occurrence

## Slide 19: Example 1
In a workshop, a painter is carrying out façade restoration using solvent-based paints. He is in contact with solvent-based paint 8 hours a day for 3 weeks and does not wear any PPE (personal protective equipment). This exposure caused a respiratory disease.
Schematize the process of the occurrence of the damage.

## Slide 20: Solution of example 1

## Slide 21: Example 2
In an industrial complex, an employee is working near an oil spill without safety shoes. One of his colleagues calls him; as he walks over the oil spill, he slips. This caused him a knee sprain.
Illustrate the process of the occurrence of the damage.

## Slide 22: Solution of example 2

## Slide 23: Example 3
An electrician is working inside an electrical cabinet where there is a live bare conductor of 230 volts. The electrician is not wearing any personal protective equipment and has bare hands.
Illustrate the process of harm occurrence.

## Slide 24: Solution of example 3
live bare conductor of 230 volts

## Slide 25: Test
In example 3 (electrician who comes into direct contact with the conductor), propose actions/barriers to prevent the damage.

## Slide 26: Solution
To prevent the occurrence of damage, it is enough to eliminate one of its components:
Person: Remote monitoring or remote diagnostics
Hazard: Isolate the conductor
Use very low voltage
Hazardous situation: Keep the conductor away from the work area
Use a screen to separate the work area from the conductor
Dangerous event: Use insulated screwdrivers
Avoidance: Work with gloves

## Slide 27: Professional situation
Mr. M.K., an operator at company R, has been working 7 hours a day for 5 years.
The operator was on site performing sandblasting and cleaning operations on a boiler. While he was responsible for monitoring and removing incineration and sandblasting residues on the conveyor to prevent clogging, he put his hand through the inspection hole up to the operating airlock, where his left-hand index, middle, and ring fingers were caught by the rotating blades of the airlock.
He later said:
The machine had become jammed and was stopped; it restarted while I had my hand inside the nozzle, trying to clear the blockage.”

## Slide 28
Questions :
Identify the occupational risk presented by this situation.
Analyze the situation by creating a diagram of the process leading to harm.
Using the following document:

## Slide 29: Assess the severity of the harm presented by the professional situation. Evaluate the likelihood of the harm occurring by completing the following table.
c) Determine the risk reduction priority level based on the following grid:
4. Propose two measures to eliminate or reduce the risk in this work situation.

## Slide 30
Réponses:
The occupational risk presented by this situation is the risk associated with work equipment.
Diagram of harm occurrence:

## Slide 31
3. a) Severity 3: SERIOUS
b)
c) Risk level :

## Slide 32
d) Reduction:
* Prohibit a hand from entering the punch hole
* Bring the machine into compliance (no accidental triggering)
* Wear gloves that can reduce the severity of the consequences

## Slide 33: Risk sheets
These risk sheets are presented in a brochure of the INRS (National Institute for Research and Safety), France.
The document is titled Assessment of Occupational Risks – Aid for Identifying Risks in SMEs-SMIs.
The sheets help the employer to initiate the evaluation process in a simple way.

## Slide 34: Risk sheets
Sheet 1: Risks of tripping, collision, or other movement disturbances
Sheet 2: Risks of falling from height
Sheet 3: Risks related to internal vehicle traffic
Sheet 4: Road risks during work missions
Sheet 5: Risks related to physical workload
Sheet 6: Risks related to mechanical handling
Sheet 7: Risks related to products, emissions, and waste
Sheet 8: Risks related to biological agents
Sheet 9: Risks related to work equipment
Sheet 10: Risks related to collapses and falling objects
Sheet 11: Risks and nuisances related to noise
Sheet 12: Risks related to thermal environments
Sheet 13: Risks of fire and explosion
Sheet 14: Risks related to electricity
Sheet 15: Risks related to lighting conditions
Sheet 16: Risks related to radiation
Sheet 17: Psychosocial risks
List of risks addressed by the INRS:

## Slide 35: Risk sheets (example)

## Slide 36: Risk sheets (example)

## Slide 37
RISKS OF SAME-LEVEL FALLS
These are accident risks that result from a person coming into sudden contact with the ground or with an object during a fall (equipment, furniture, machine).
Slippery floor (spilled substances such as water, oil, diesel fuel, debris…)
Uneven or defective floor (small step, platform, slope break, damaged flooring, roughness, holes, loose tiles…)
Clutter (obstructed passageway, tools, electrical cables)
Slippery or non-compliant stairs PREVENT
Keep passageways clear of any objects
Tidy up the work area at the end of the task
Immediately absorb any spills
Mark existing hazards: slope break or slippery floor

## Slide 38: ROAD RISK
It is a traffic-related accident risk associated with the travel of an employee carrying out a work assignment on behalf of the company, or traveling between home and the workplace.
Constraints related to organization: frequent changes of work locations, time pressure, driving distance and duration, absence of an accompanying person…
It is also the consequence of:
Loadings Vehicle condition Alcohol, drugs, fatigue
Constraints related to communications: mobile phone, CB radio, activities while driving (reading a map, changing a CD, lighting cigarettes…)
51

## Slide 39: Prevent road risk
Organize travel
→ Scheduling appointments
→ Delivery planning
Manage the vehicle fleet
→ Choice of vehicle used
→ Safety equipment
→ Maintenance and servicing
Employee skills
→ Training plans
→ Awareness workshops
Communication practices
→ Secure communication protocol
52

## Slide 40: RISKS RELATED TO PHYSICAL ACTIVITY
These are accident and/or occupational disease risks affecting the trunk, upper, and lower limbs, resulting from awkward postures, intense and/or repetitive physical efforts, crushing, or impacts.
Musculoskeletal disorders (MSDs) are the most common and widespread occupational diseases.
Repetitive handling of loads with unit weights: unloading small-sized boxes, emptying containers, retrieving loads from heights…
Tasks requiring repetitive movements: meat cutting, assembly line work, office activities (mouse, keyboard…), stamping, gluing, sewing, sanding…
Tasks requiring maintaining a posture: screen work, watchmaking, mechanical work, work in confined spaces…

## Slide 41: Prevent risks related to physical activity
Use handling tools
Train staff in PRAP (Prevention of Risks Related to Physical Activity)
Arrange and organize workstations to minimize effort (integrate ergonomics into the workstation).
Carpal tunnel syndrome is the most common musculoskeletal disorder (MSD) of the upper limb.

## Slide 42: These occupational risks affect the mental well-being of employees (stress, harassment, workplace violence, etc.).
PSYCHOSOCIAL RISKS
Hazardous situations
Physical or verbal assaults
Unclear assigned tasks (how should I proceed?…)
High quantitative demands (time pressure…)
Job insecurity
Disrespectful behavior toward a person (abuse, insults), biased remarks
Frequent absences

## Slide 43: Prevent psychosocial risks
Establish a diagnosis of work relationships and a plan for improving the quality of work relations
Act on management and organization
Promote recognition and professional development of employees
Encourage communication and dialogue

## Slide 44: RISKS RELATED TO INTERNAL TRAFFIC
These are risks resulting from a person being struck by a vehicle (motorcycle, car, truck, earthmoving equipment, lifting device, mainly forklifts).
These are risks that can also result from the collision of two vehicles with each other or with an obstacle within the company premises.
These are risks whose consequences can be very severe, especially since the energies involved are significant (speed, mass).
Existence of shared traffic zones: for pedestrians and vehicles, intersections, passing nearby, dust, exhaust, falling objects…
Dangerous traffic routes: narrow, sloped, with limited visibility, cluttered, in poor condition, slippery…
57

## Slide 45: Prevent risks related to internal traffic
Develop a traffic plan: traffic direction, restricted access, speed limits, signage distinguishing pedestrian routes
Install warning and traffic signs
Regularly inspect the condition of vehicles and their safety equipment

## Slide 46
RISKS RELATED TO THERMAL ENVIRONMENTS
These are health risks (discomfort, fatigue, malaise) if thermal conditions are unsuitable.
Work performed at unsuitable temperatures: lack of air conditioning or heating, exposure to the sun or bad weather causing high or low temperatures, work in cold rooms.
Work performed under specific temperatures: unusual temperatures or climatic conditions, wind, rain, drafts…

## Slide 47: Prevent risks related to thermal environments
Arrange breaks in a temperate area for staff working in very hot or very cold environments
Provide appropriate personal protective equipment
Make water stations available to staff

## Slide 48: RISKS RELATED TO THE USE OF CHEMICAL PRODUCTS
These are risks of infection, allergy, burns, or poisoning through inhalation, ingestion, or skin contact with substances used or released as gases, solid particles, or liquids.
Under certain conditions, this can constitute an occupational disease risk.
Dust emissions: metal, wood dust, cement, asbestos, flour, silica, coal, sulfur…
Gas emissions (heating devices), aerosol gases (oil vapor, gas, substances), vapors (cellulose-based paints, alkyd paints, lead-based paints, varnishes, resins, thinners)
Smoke emissions: welding, exhaust gases, various combustions…
61

## Slide 49: Prevent risks related to the use of chemical products
Check the toxicity and labeling of products
Inform employees about the hazards of each product used (by reading the label and the safety data sheet).
Look for less hazardous substitute products!
Implement a system to capture emissions
Provide appropriate personal protective equipment
62

## Slide 50: RISKS RELATED TO MACHINES AND TOOLS
These are accident risks caused by mechanical action (cutting, piercing, crushing, etc.) from a machine, a part of a machine, or a handheld, manual, or fixed tool.
Work with tools that have moving parts: transmission components,
pulleys, belts, chains, cables, moving parts…
Work with sharp or abrasive tools… generally, machine tools.
Work on machines using pressurized fluids: hydraulic, pneumatic (compressed air)…
63
Work requiring lockout/tagout procedures: maintenance and repair work, additional installation, retrieval of a jammed or stuck part, energy release, end of mechanical movement…

## Slide 52: RISKS RELATED TO NOISE HAZARDS
These are accident risks caused by discomfort, interference with verbal communication, and hindrance during the performance of delicate tasks.
They are also occupational disease risks in cases of prolonged exposure: hearing loss is irreversible. These risks are common in certain professional activities.
Continuous noise emitted by machines or tools: compressors, engines, loudspeakers, printers, jackhammers, etc.
Impulse noise: vents, compressed air releases, audible signals other than alarm sirens…Une perte de l’audition est irréversible
Hearing loss is irreversible.

## Slide 53: RISKS OF FALLING FROM HEIGHT
These are accident risks resulting from a person coming into sudden contact with the ground or an object during a fall. The consequences can be very severe, especially when the height difference is significant.
Areas with lower-level parts: stairs, walkways, docks, pits, tanks, hoppers, trapdoors…
Access to elevated parts: cabinets, shelves, lighting fixtures, roofs, truck tarps, vehicles on a lift, etc.
Use of mobile devices: ladder, stepladder, rolling or fixed scaffolding.
Use of improvised means: chair, boxes, crates, stacked objects or furniture, storage racks, buckets, and forks…

## Slide 54: Prevent the risk of falling from height
Install collective protection systems (guardrails, safety nets, lifelines).
Provide appropriate access equipment (scaffolding).
Prohibit risky behaviors
Provide personal protective equipment (safety harnesses).

## Slide 55: RISKS RELATED TO COLLAPSES AND FALLING OBJECTS
These are accident risks resulting from objects falling from storage or high shelving, from an upper floor, or from the collapse of materials.
Work carried out in trenches, wells, or tunnels: Shoring is mandatory for trenches deeper than 1.30 m and with a width equal to or less than two-thirds of the depth (Art. 66, Resolution 35CP).
Objects stacked at a great height: grates, scaffolding, roofs, pallets, crates, containers, tree trunks, planks…
Objects or goods stored at height: storage racks, shelves, tops of cabinets, construction phases, lifting and transport of materials, etc.

## Slide 56: Prevent risks related to falling objects and collapses
Proper storage of loads; do not overload the rack.
Wear personal protective equipment.
Follow the trench shielding rules.
Monitor old stockpiles
IAP/A.E.M
69